## Slide 1: Simulation of Wi-Fi based TSN Mechanisms using NS-3 Simulator
Prof. Dr.-Ing. Axel Sikora
Manuel Schappacher
Jubin Sebastian Elayanithottathil
Aneemesh Vidyarthi
WiFi 6 AX, FTM, TWT and QoS

## Slide 2: Contents
Background
Implementation
  Composition
    Architecture
    Notes
  Methodology
    Points
    Timeline
References

## Slide 3: Background
ivESK works on Time Sensitive Networks (TSN) for industrial communications
TSN uses accurate time sync (802.1AS) and scheduling like Time Aware Shapers (802.1Qbv)
TSN is technology-agnostic but Wi-Fi has challenges like asymmetric paths, unreliable links
Wi-Fi has different protocols than Ethernet TSN e.g. Fine Time Measurement (FTM), Access Categories (AC)
Goal is to create ns-3 simulations to model Wi-Fi based TSN
Will integrate/modify existing ns-3 models like Wi-Fi, FTM, PTP, Qbv Ethernet
This will setup a simulation framework to evaluate parameters and behavior of TSN over Wi-Fi

## Slide 4: Implementation – Composition – Architecture

## Slide 5: Implementation – Composition – Notes
1 broadcasting AP, several STA endpoints
  Classified for real-time, best effort etc for different use cases per endpoint (QoS)
  TSN switches connected to TSN WLAN region
  Clocks per node. (GM is TSN switch)
  TWT based sleep/wake for STAs (Wi-Fi 6 spec)
More APs for interference testing
  FTM in place of gPTP for wireless time sync for STA and APs
Time-Aware Shaper
  IEEE 802.1Qbv on wired TSN switch
  We do not use Qbu and br, frame pre-emption not possible on Wi-Fi 6
Wi-Fi QoS implementation for minimizing interference
  Best effort, video, voice, background ACs
  Queue Discs to define priority levels for different ACs (derived from TAS)
  We use BE (best effort) for defining realtime traffic

## Slide 6: Implementation – Methodology – Points
TSN-enabled switch connected to Wi-Fi 6 enabled stations using FTM for time sync
Attempt to implement Wi-Fi QoS on stations and AP to mitigate latency with traffic classification
  ns-3 QoS tagging and queues on the Wi-Fi net devices
  ns3::EdcaTxop defines access classes (BE, Vi, Vo, Bg,)
  QosWifiMacHelper attribute using smart pointer to WifiMac objects (AP and STA)
  Traffic control queues mapped to different Wi-Fi AC priorities (QueueDiscContainer)
  QoS tagging rules on all sockets to enable datagram flags
  Contention Window – Backoff algorithm – Randomized time slot allocation
Time-Aware Shaper on wired TSN switch. (IEEE 802.1Qbv)
Isolated channel using OFDMA for multiple resource units on the same channel (optional)
Goals:
  Deterministic Networking
  Minimizing Jitter and Latency
  Spectrum efficiency and isolation (optional)

## Slide 7: Implementation – Methodology – Timeline

## Slide 8: References
https://www.nsnam.org/docs/
IEEE 1588 documentation for standards used
https://www.youtube.com/watch?v=K3H9L6FM-xo
https://www.researchgate.net/profile/Dennis-Krummacker/publication/348431501_TSN_Simulation_Time-Aware_Shaper_implemented_in_ns-3/links/5ffec2c0299bf140888ff7cd/TSN-Simulation-Time-Aware-Shaper-implemented-in-ns-3.pdf
https://groups.google.com/g/ns-3-users/c/idtjCwij-lE?pli=1
https://www.nsnam.org/docs/release/3.28/doxygen/classns3_1_1_edca_txop_n.html#details
https://www.nsnam.org/docs/release/3.24/doxygen/classns3_1_1_dca_txop.html