Simulation of Wi-Fi based TSN Mechanisms using
NS-3 Simulator
Simulation of Wi-Fi based TSN Mechanisms using
NS-3 Simulator
Prof. Dr.-Ing. Axel Sikora
Manuel Schappacher
Jubin Sebastian Elayanithottathil
Aneemesh Vidyarthi

---
Contents
Contents
- Background
- Implementation
  - Composition
    - Architecture
    - Notes
  - Methodology
    - Points
    - Application Diagram
- References

---
Background
Background
- ivESK works on Time Sensitive Networks (TSN) for industrial communications
- TSN uses accurate time sync (802.1AS) and scheduling like Time Aware Shapers (802.1Qbv)
- TSN is technology-agnostic but Wi-Fi has challenges like asymmetric paths, unreliable links
- Wi-Fi has different protocols to fulfil TSN goals e.g. Fine Time Measurement (FTM), Access Categories (AC) and lacks support for frame-preemption.
- The goal is to create ns-3 simulations to model Wi-Fi based TSN.
- One avenue of optimization: application-based definitive priority on traffic from wireless nodes - Wi-Fi QoS

---
Implementation – Composition – Architecture
Implementation – Composition – Architecture
The architecture details the class-object structure used to design the physical topology that is used in the simulation
The QoS setting is enabled by:
modifying wifi-setup.cc,
porting qos-txop.cc (deprecated),
InetSocketAddress ToS parameters
Access Category Matrix, native to ns-3.26+ defines user priorities.
QoS-txop.cc defines ACs on a hardware level while InetSocketAddress does it on a per-application, per-port basis.
- Advantages...

---
Implementation – Composition – Notes
Implementation – Composition – Notes
1 broadcasting AP, several STA endpoints
  - Classified for real-time, best effort etc for different use cases per endpoint (QoS)
  - TSN switches connected to TSN WLAN region
  - Clocks per node. (GM is TSN switch as per gPTP specification)
  - TWT based sleep/wake for STAs (Wi-Fi 6)
  - FTM to obtain Wi-Fi communication timestamps is to be implemented using ftm-sync.h
- Time-Aware Shaper
  - TAS (IEEE 802.1Qbv) on both switches, using schedules
  - Time synchronization with callback to Simulator::Now()*
- Wi-Fi QoS implementation
  - Application flow between wired and wireless nodes with InetSocketAddress objects
  - TOS socket tagging (simulated, port-specific) from matrix specified in ns-3 docs.
- Build system ported to ns-3.36.1 (new CMake-based ns3 system used instead of the older WAF system)
- Testing: https://docs.google.com/spreadsheets/d/1KQKjGEhCIMj2iP7ncDUTTquqrSq4hpVmSAhxCtsc7W4/edit#gid=0

---
Implementation – Methodology – Points
Implementation – Methodology – Points
- TSN-enabled switch and nodes connected to Wi-Fi 6 AP with its own switch.
- The simulation uses PerfectClockModel for time sync.
- Attempt to implement Wi-Fi QoS on stations and AP to mitigate latency with traffic classification
  - wifi-setup.cc – QosSupported flag on ApWifiMac and StaWifiMac objects that are used for initializing wireless device containers.
  - ns3::WifiMacHelper defines access classes according to a matrix consisting of User Prio and AC
  - InetSocketAddress objects define QoS per application, per port.
- Time-Aware Shaper on wired and AP switches.
- Wired and wireless stations talk to each other with different levels of priority.
- Flow monitoring and packet capture. 7 UDP flows exist in the simulation.
- Goals:
  - Deterministic Networking
  - Minimizing Jitter and Latency
  - Application priority segregation

---
Implementation – Methodology – Timeline
Implementation – Methodology – Application Diagram

---
References
Documentation and References
- https://probable-tarsier-b33.notion.site/Wi-Fi-QoS-bridged-to-TSN-topology-fbee240c0fdf46f3a43604b78b685308?pvs=4
- https://git.fortiss.org/iiot_external/detnetwifi-ns3 (initial code)
- https://git.fortiss.org/iiot_external/ns-3-detnetwifi/documentation
- https://www.nsnam.org/docs/3.34
- https://www.nsnam.org/docs/3.36
- IEEE 1588 documentation for standards used
- https://www.researchgate.net/profile/Dennis-Krummacker/publication/348431501_TSN_Simulation_Time-Aware_Shaper_implemented_in_ns-3/links/5ffec2c0299bf140888ff7cd/TSN-Simulation-Time-Aware-Shaper-implemented-in-ns-3.pdf
- https://groups.google.com/g/ns-3-users/c/YuD49ScDb1Y?pli=1 (debugging using WAF)
- https://github.com/tkn-tub/wifi-ftm-ns3